Building a Linux Router From Scratch
Michael Marley

---
What is a router?
?

---
What is a router?
Most residential ISPs give you a single IPv4 address and (if you’re lucky) a prefix (allotment) of IPv6 addresses

---
What is IPv4?
- IPv4 is the legacy standard for addressing computers on the Internet. 4,294,967,296 addresses are available (32-bit address space)
- The address space is running out, which is part of the reason why a router is required in the first place

---
What is NAT?
- NAT (Network Address Translation) is a process by which the router multiplexes connections from multiple devices into a single IP address
- More on this later

---
What is IPv6?
- IPv6 is the replacement for IPv4, with 340,282,366,920,938,463,463,374,607,431,768,211,456 addresses available (128-bit address space)
- Because of the vast increase in address space, no NAT is necessary and the ISP gives you many IPv6 addresses (or at least it should)

---
What does a router do?
- Assigns IPv4, IPv6 addresses to local devices
- Performs NAT on IPv4 connections
- Configurably blocks incoming connections from the Internet (firewall)
- Often provides other services like DNS (converts hostnames to IP addresses)

---
So how do we build a router?
- First, we need to configure the router’s upstream connection to the ISP (Wide Area Network, or WAN for short)
- For the purposes of this presentation, we will use systemd-networkd

---
WAN configuration (IPv4)
/etc/systemd/network/eno1.network:
[Match]
Name=eno1
[Network]
DHCP=ipv4
IPv6AcceptRA=no
[DHCP]
UseDNS=no
UseHostname=no
UseNTP=no

---
So how do we build a router?
- Next, we need to configure the LAN interfaces (the one pointed toward the local devices)
- We’re going to use multiple LAN subnets so we can have our trusted devices (fire)walled off from guest devices and insecure IoT devices.

---
How do you have multiple LANs?
- The router only has two physical interfaces
- Therefore, we must use VLANs (Virtual LANs) to multiplex multiple LAN subnets into a single interface

---
VLAN configuration
/etc/systemd/network/enp1s0.network:
[Match]
Name=enp1s0
[Network]
VLAN=enp1s0.1
VLAN=enp1s0.2
VLAN=enp1s0.3
VLAN=enp1s0.4
VLAN=enp1s0.5
ConfigureWithoutCarrier=yes
IgnoreCarrierLoss=yes
KeepConfiguration=yes
[Link]
RequiredForOnline=no

---
LAN device configuration
/etc/systemd/network/enp1s0.1.netdev:
[NetDev]
Name=enp1s0.1
Kind=vlan
[VLAN]
Id=1

---
LAN network configuration
/etc/systemd/network/enp1s0.1.network:
[Match]
Name=enp1s0.1
[Network]
Address=10.1.0.1/16
Address=fdda:5f29:421b:1::1/64
IPForward=yes
ConfigureWithoutCarrier=yes
IgnoreCarrierLoss=yes
KeepConfiguration=yes
[IPv6Prefix]
Prefix=fdda:5f29:421b:1::/64
[Link]
RequiredForOnline=no

---
What do all those numbers mean?
- 10.1.0.1 is the local IPv4 address assigned to the router
- 10.0.0.0/8 (along with 192.168.0.0/16 and 172.16.0.0/20) are private IPv4 spaces, meaning they cannot be routed on the public Internet

---
What do all those numbers mean?
- fdda:5f29:421b:1::1/64 is the local IPv6 address assigned to the router
- fdda:5f29:421b:1::/64 is the local IPv6 prefix assigned to the router, from which the router assigns addresses to local clients
- fd00::/8 is the private IPv6 space, functioning the same way as the private IPv4 space

---
LAN configuration
For more LAN subnets, just repeat the device and network configurations, incrementing the numbers

---
WAN configuration (IPv6)
- systemd-networkd isn’t featureful enough yet to be able to handle the IPv6 WAN properly
- So, we use wide-dhcpv6c instead

---
WAN configuration (IPv6)
/etc/wide-dhcpv6/dhcp6c.conf:
interface eno1 {
        send ia-pd 1;
        send ia-na 1;
};
id-assoc na 1 {
};
id-assoc pd 1 {
        prefix ::/56 infinity;
        prefix-interface enp1s0.1 {
        sla-id 1;
        sla-len 8;
        };
        prefix-interface enp1s0.2 {
        sla-id 2;
        sla-len 8;
        };
        prefix-interface enp1s0.3 {
        sla-id 3;
        sla-len 8;
        };
        prefix-interface enp1s0.4 {
        sla-id 4;
        sla-len 8;
        };
        prefix-interface enp1s0.5 {
        sla-id 5;
        sla-len 8;
        };
};

---
Are we done yet?
Not even close

---
DHCP server
- The DHCP (or Dynamic Host Control Protocol) server’s job is to assign local IPv4 and IPv6 addresses to the devices within the network
- For this task, we use dnsmasq
- Again, the configuration needs to be repeated for each local subnet

---
DHCP server configuration
/etc/dnsmasq.conf:
port=10053
server=::1#10053
no-resolv
no-hosts
dhcp-authoritative
dhcp-rapid-commit
local=/lan/
domain=lan
interface=enp1s0.1
dhcp-range=interface:enp1s0.1,10.1.0.2,10.1.255.253,1h
dhcp-range=interface:enp1s0.1,fdda:5f29:421b:1::2,fdda:5f29:421b:1::ffff,64,1h
dhcp-option=enp1s0.1,option:dns-server,10.1.0.1
dhcp-option=enp1s0.1,option:ntp-server,10.1.0.1
dhcp-option=enp1s0.1,option6:ntp-server,[fdda:5f29:421b:1::1]
dhcp-option=enp1s0.1,option6:dns-server,[fdda:5f29:421b:1::1]

---
RA/SLAAC server
- The Stateless Address Auto-Configuration (SLAAC) server’s job is to assign local and global IPv6 addresses to local devices by sending Router Advertisements (RAs).
- For this we use radvd
- dnsmasq supports sending RAs as well, but it can be problematic with dynamic prefixes

---
SLAAC server configuration
/etc/radvd.conf:
interface enp1s0.1 {
        AdvSendAdvert on;
        AdvManagedFlag on;
        AdvOtherConfigFlag on;
        MaxRtrAdvInterval 30;
        prefix ::/64 {
        AdvOnLink on;
        AdvAutonomous on;
        AdvRouterAddr on;
        };
        RDNSS fdda:5f29:421b:1::1 {
        AdvRDNSSLifetime 6000;
        };
        DNSSL lan {
        AdvDNSSLLifetime 6000;
        };
};

---
Firewall
- For firewalling, we use nftables
- This is a replacement to the well-known iptables that uses a much more elegant and simple syntax
- The configuration is too long to fit on a slide

---
DNS
- For DNS, we use unbound
- dnsmasq already covers local DNS, but we must configure unbound to forward local requests
- This presentation covers only a basic setup; optimizations, DNS-over-TLS, etc. are a topic for another presentation

---
DNS configuration
/etc/unbound/unbound.conf.d/block-rebind.conf:
server:
        private-address: 10.0.0.0/8
        private-address: 172.16.0.0/12
        private-address: 192.168.0.0/16
        private-address: 169.254.0.0/16
        private-address: fd00::/8
        private-address: fe80::/10
        private-address: ::ffff:0:0/96

---
DNS configuration
/etc/unbound/unbound.conf.d/listen-all-ports.conf:
server:
        interface: ::0
        interface: 0.0.0.0
        access-control: 0.0.0.0/0 allow
        access-control: ::0/0 allow

---
DNS configuration
/etc/unbound/unbound.conf.d/listen-all-ports.conf:
server:
        do-not-query-localhost: no
        local-zone: "lan." always_nxdomain
        private-domain: "lan."
        domain-insecure: "lan"
        local-zone: "10.in-addr.arpa." always_nxdomain
        private-domain: "10.in-addr.arpa."
        domain-insecure: "10.in-addr.arpa"
        local-zone: "b.1.2.4.9.2.f.5.a.d.d.f.ip6.arpa." always_nxdomain
        private-domain: "b.1.2.4.9.2.f.5.a.d.d.f.ip6.arpa."
        domain-insecure: "b.1.2.4.9.2.f.5.a.d.d.f.ip6.arpa"
        access-control-view: 127.0.0.0/8 localdnsview
        access-control-view: 10.0.0.0/8 localdnsview
        access-control-view: ::1/128 localdnsview
        access-control-view: fd00::/8 localdnsview
view:
        name: "localdnsview"
        local-zone: "use-application-dns.net" always_nxdomain
        local-zone: "lan." transparent
        local-zone: "10.in-addr.arpa." transparent
        local-zone: "b.1.2.4.9.2.f.5.a.d.d.f.ip6.arpa." transparent
forward-zone:
        name: "lan."
        forward-addr: ::1@10053
forward-zone:
        name: "10.in-addr.arpa."
        forward-addr: ::1@10053
forward-zone:
        name: "b.1.2.4.9.2.f.5.a.d.d.f.ip6.arpa."
        forward-addr: ::1@10053

---
NTP
- For DNS, we use chrony
- No configuration to cover here; just put “allow” at the bottom of /etc/chrony/chrony.conf to allow access to the server

---
Quality-of-Service (QOS)
- For QOS, we use cake
- This is the same queue discipline used by OpenWRT’s sqm-scripts
- The purpose is to automatically prioritize traffic like VoIP and gaming while preventing high latency due to bufferbloat

---
Cake setup script
/usr/local/bin/cake-setup:
#!/bin/sh
DOWNLOADBANDWIDTH="235Mbit"
UPLOADBANDWIDTH="23500Kbit"
IFBSUFFIX="ifb"
if [ -z "$1" ]; then
        echo "Interface name must be passed as first command-line argument!"
        exit 1
fi
tc qdisc add dev $1 root cake bandwidth $UPLOADBANDWIDTH nat ack-filter docsis
ip link add name $1$IFBSUFFIX type ifb
tc qdisc del dev $1 ingress
tc qdisc add dev $1 handle ffff: ingress
tc qdisc del dev $1$IFBSUFFIX root
tc qdisc add dev $1$IFBSUFFIX root cake bandwidth $DOWNLOADBANDWIDTH besteffort nat ack-filter wash docsis
ip link set dev $1$IFBSUFFIX up
tc filter add dev $1 parent ffff: protocol all prio 10 u32 match u32 0 0 flowid 1:1 action mirred egress redirect dev $1$IFBSUFFIX
exit 0

---
FAQ
- Why didn’t you use pfSense?
- Why didn’t you use OpenWRT?

---
Why didn’t I use pfSense?
- Simply put, pfSense sucks:
  - Flaky IPv6 autoconfiguration
    - Sometimes it just doesn’t work
    - It often requires manual intervention to restore IPv6 addressing after a WAN outage
  - No IPv6 local addressing support
    - (Local IPv6 communication is lost if the WAN goes down)
  - Difficult, unintuitive firewall setup
    - No ability to refer to “the Internet” in a rule
  - Poor/unusable QOS
    - Only egress shaping is allowed; ingress shaping is done by doing egress shaping on each LAN interface
      - QOS rules therefore needlessly affect intra-LAN traffic
      - Heavy download traffic to multiple subnets simultaneously breaks the “ingress” limit and causes bufferbloat and high lag.
  - Poor default DNS configuration
    - Unbound restarts whenever a client requests DHCP, causing a (short) outage(!)
  - Flaky upgrades
  - Probably a bunch of other stuff I have forgotten as well

---
Why didn’t I use OpenWRT?
- I actually did, for quite a while
- OpenWRT is a very high-quality product
- I stopped mainly because the architecture isn’t really designed for running on PC-style hardware, requiring self-compilation in a number of cases

---
Other questions?

---
Thanks!